# 1) Time & TF backbone
- EKF / odom: Your EKF (separate file) fuses /wheel/odom + IMU and publishes odom → base_link.
- Global pose: Because you’re running slam_toolbox (online_async), it publishes map → odom.
- Net effect: Nav2 nodes can transform any data between map / odom / base_link.
# 2) Localization block in your YAML
The amcl: block you showed is not used when you run SLAM. (AMCL + map_server are for localization on a fixed map.) It can sit there harmlessly; slam_toolbox supplies map→odom.
# 3) Costmaps (what the robot “sees”)
You defined two costmaps:
Local costmap (local_costmap):
- Frame: odom, Base: base_link, rolling window 3×3 m, 0.05 m resolution.
- Plugins: voxel_layer (using /planar_laser/scan) + inflation_layer (radius 0.80 m).
- Used for short-range obstacle avoidance by the controller.
Global costmap (global_costmap):
- Frame: map, Base: base_link, 0.05 m resolution, tracks unknown.
- Plugins: static_layer (subscribes to /map from SLAM), obstacle_layer (same laser), inflation_layer (0.8 m).
- Used by the planner to compute long paths.
Costmap filters (keepout_filter, speed_filter) are listed but enabled: false, so they’re instantiated and subscribe to filter-info topics, but they don’t change costs (those “Filter mask was not received” warnings are benign when disabled).
# 4) Global planner
- Node: planner_server with NavfnPlanner (“GridBased”), allow_unknown: true, tolerance: 0.5.
- It reads the global costmap and produces a path in map frame. In your logs you see “Passing new path to controller.” That means planning works.
# 5) Controller (turns path into velocity)
- Node: controller_server, plugin nav2_mppi_controller::MPPIController at 20 Hz (controller_frequency).
- Consumes:
  - The local costmap (for near obstacles),
  - The planned path,
  - TF (to know where you are).
- Outputs raw cmd_vel to the Velocity Smoother.
Your MPPI settings look consistent for a diff-drive: motion_model: DiffDrive, vx_max 0.5, wz_max 1.9, critics enabled, etc.
# 6) Velocity Smoother
- Node: velocity_smoother (“OPEN_LOOP”), 20 Hz, odom_topic: odom.
- It smooths the controller’s commands and publishes /cmd_vel_smoothed.
# 7) Safety gate (Collision Monitor)
- Node: collision_monitor subscribes to /cmd_vel_smoothed and laser, simulates near-future collisions, and only then republishes to /cmd_vel (the one Gazebo consumes).
- It also listens to the local footprint topic from the local costmap and runs an “approach” polygon check.
✅ Important tiny bug in your YAML:
In this block you currently have:
collision_monitor:
  ...
  observation_sources: ["scan"]
  scan:
    type: "scan" # <-- this should be "LaserScan"
    topic: "/planar_laser/scan"
type must be the message type string "LaserScan" (exactly), not "scan".
With the wrong type, the source is considered invalid, and the monitor will publish stops, which matches your earlier log:
[collision_monitor]: Robot to stop due to invalid source...
Fix:
collision_monitor:
  ros__parameters:
    ...
    observation_sources: ["scan"]
    scan:
      type: "LaserScan"
      topic: "/planar_laser/scan"
      min_height: 0.15
      max_height: 2.0
      enabled: True
# 8) Behavior Tree orchestrator
- Node: bt_navigator runs the NavigateToPose tree. It sequences:
  - Compute path (planner_server)
  - Smooth path (smoother_server)
  - Follow path (controller_server → velocity_smoother → collision_monitor)
  - Recovery behaviors if needed (spin/backup/etc.)
Your bt_loop_duration: 10 means the BT ticks frequently (10 ms default in Nav2).
# 9) Command reaches Gazebo
- ros_gz_bridge forwards ROS /cmd_vel → Gazebo /cmd_vel.
- Gazebo’s DiffDrive consumes it and moves the robot.
- Gazebo publishes /odom → bridged to /wheel/odom → EKF → odom→base_link, closing the loop.

## Why “no /cmd_vel” happens & how to confirm quickly
Given your config and logs, the most likely reason for zero /cmd_vel is the Collision Monitor blocking due to the bad type. Here’s the fastest sanity path:
1. Fix the collision_monitor.scan.type to "LaserScan" and relaunch.
2. Watch the chain:
  1. ros2 topic echo /cmd_vel_smoothed (should be non-zero while navigating)
  2. ros2 topic echo /cmd_vel (should now mirror it)
3. If /cmd_vel_smoothed is zero:
  1. Check controller health: ros2 topic echo /local_costmap/costmap (non-empty), TF (ros2 run tf2_tools view_frames), and controller warnings.
4. If /cmd_vel_smoothed non-zero but /cmd_vel still zero:
  1. Then the Collision Monitor is still stopping you; ros2 topic echo /collision_monitor_state will say STOP if a source is invalid or it predicts a collision.

## TL;DR flow (with your params)
Laser /planar_laser/scan → Local/Global costmaps → Planner (path in map) → MPPI controller (20 Hz, uses odom local costmap) → Velocity Smoother → Collision Monitor (laser + footprint) → /cmd_vel → ros_gz_bridge → Gazebo DiffDrive → /wheel/odom → EKF → odom→base_link, and slam_toolbox provides map→odom.